## Slide 1: AOC Proposal
第三組 - 大禹治水，小郭治洪

## Slide 2
黃雍翔
陳冠穎
王文楷
Member List
黃雍翔：Model design、Model training
陳冠穎：DMA design、PE design
王文楷： DMA design、PE design

## Slide 3
Member List
蔡明翰
胡家豪
蔡明翰： DMA design、PE design
胡家豪： Model design、Power unit design

## Slide 4: Outline
Purpose
Basis
System overview
DLA architecture & Memory hierarchy
Dataflow & Network on chip
Analysis
Innovation

## Slide 5
As neural networks advance, a large number of parameters can burden memory resources.
Heavy computational demands on mobile devices can lead to significant power consumption
Purpose

## Slide 6
Basis- MobileNet V3
Separate the normal convolution to Depthwise convolution and pointwise convolution to reduce parameters
Adding Squeeze-and-Excitation (SE) block to increase accuracy
Replace ReLU with h-Swish activation function to capture more non-linear relationship

## Slide 7
Normal convolution

## Slide 8
Depthwise convolution & Pointwise convolution
(a) Depthwise convolution
(b) Pointwise convolution

## Slide 9
Squeeze-and-Excitation block
Different choice of Nonlinearities
(a) SE block
(b) SE module
(c) Activation comparison

## Slide 10
System overview

## Slide 11
Supported tasks
Standard convolution
Depthwise convolution
Pointwise convolution
Average & Max pooling
Fully connected layer
Residual
Relu
h-Swish

## Slide 12
DLA architecture & Memory hierarchy

## Slide 13
Network on chip

## Slide 15
Mapping optimization - Depthwise convolution

## Slide 16
Mapping optimization - pointwise convolution

## Slide 17
Analysis
DRAM Storage size : 512MB
  DRAM size of Pynq z2
DLA Storage size :
  Ping-Pong SRAM : 512 KB
    112×112×16 = 196 KB
  Weight SRAM : 96 KB
    144×576 = 81 KB
  Buffer size：3 KB
    32 bits + 8bits +3 × (16×16×4)

## Slide 18
Analysis
Synthesize a single PE under U18 process：
  Area：5400747-5344503 = 56244 um2
  Power：1.2203-1.2171 = 0.01mW
(b) With SRAM and MAC
(a) Only with SRAM

## Slide 19
Roofline model calculation
Memory BW | Memory access amount × byte × frequency = = 3.2 GB/s
Peak performance | PE numbers × MAC × frequency = = 0.0512 TOPs
Arithmetic Intensity | Peak performance / Memory BW = 0.0512 / 0.0032= 16
Memory BW | 
Peak performance | 
Arithmetic Intensity | Peak performance / Memory BW = 0.0512 / 0.0032= 16
TOPs/s
TOP/byte
16
0.0032

## Slide 20
Evaluation

## Slide 21
Innovation
Pruning
Power Management
Low Power design
Hardware Reuse

## Slide 22
Pruning
Picture from：An Entropy-based Pruning Method for CNN Compression, https://www.semanticscholar.org/paper/An-Entropy-based-Pruning-Method-for-CNN-Compression-Luo-Wu/cda2f01d90d98b71a49b00e34bdc03dc17d67da4

## Slide 23
Power Management
Power State | CPU | DLA
Normal | 1.8V | 1.8V
Low Power | 1.6V | 1.6V
Power control by Power management Unit
Apply by using
  Power switch
  Isolation
  Level shifter
  Retention

## Slide 24
Low Power design
Use zero gating to reduce power consumption because high-zero sparsity
0

## Slide 25
Low Power design
Use zero gating to reduce power consumption because high-zero sparsity
0

## Slide 26
Global Average Pooling

## Slide 27
Global Average Pooling

## Slide 28
Global Average Pooling

## Slide 29
Global Average Pooling

## Slide 30
Global Average Pooling

## Slide 31
Global Average Pooling
Achieve global average pooling with systolic array reuse

## Slide 32
0430~
0507
0508~
0514
0515~
0522
0522~
0531
0601~
0618
Roadmap
Model evaluation
Model Training &
Finish testbench
Hardware
implementation
Functional
verification
Hardware synthesize &
APR

## Slide 33: Reference
Howard, Andrew, et al. "Searching for mobilenetv3." Proceedings of the IEEE/CVF international conference on computer vision. 2019.
Han, Song, Huizi Mao, and William J. Dally. "Deep compression: Compressing deep neural networks with pruning, trained quantization and huffman coding." arXiv preprint arXiv:1510.00149 (2015).
Hu, Jie, Li Shen, and Gang Sun. "Squeeze-and-excitation networks." Proceedings of the IEEE conference on computer vision and pattern recognition. 2018.
Chong, Yi Sheng, et al. "An energy-efficient convolution unit for depthwise separable convolutional neural networks." 2021 IEEE International Symposium on Circuits and Systems (ISCAS). IEEE, 2021.

## Slide 34: Q & A